## Slide 1
KX-HTS Step by Step Guide Initial Set-up
September 1, 2016
Specifications are subject to change without notice.
Panasonic System Networks PBX SE team

## Slide 2
KX-HTS can be installed very easily. Only Plug and Play are required for basic use. Basic settings are programmed automatically after initialize. - All extension users can make a call to analog CO. - All extension users can receive a call from analog CO. Plug and Play even for KX-HDV SIP phone !
< Easy Cabling > 2 RJ45 jacks for 2 KX-HDV phones
1. Very Easy Installation
KX-HTS
T : Tip R : Ring
…..
Each RJ11 jack for each CO or SLT port
101 102 103 104 …. 124
SLT = Analog Single Line Telephone
PoE is not supported. L2-switch is required for 3 or more SIP phones.
Notes: 2

## Slide 3
Manual (PDF) and latest software for this product are available on the following Panasonic web site: http://www.panasonic.net/pcc/support/pbx/ Some of the documentation requires the following password : 2ufrompanasonic Leaflet is packed in KX-HTS for this information. This document (Step by step guide) explains summary only. It is important to read manuals and leaflet before selling and installing this product.
2. Manual (PDF) and Software
Notes: 3

## Slide 4
Software of KX-HTS, KX-HDV and KX-NTV has to be latest.
KX-HTS version 1.5 supports followings. (1) Phone book on LCD of KX-HDV by PBX system speed dial (2) CO button of KX-HDV230 (3) Conference by SLT
Software version up of KX-HDV phone is also required for (1) and (2).
Software of KX-NTV has to be version 0101e or later. If software version is 0101d (first mass production version), KX-NTV cannot be connected to KX-HTS. (KX-NTV first version can be connected to KX-NS/NSX only.)
3. Software Version
KX-HDV except KX-HDV230 does not support CO button.
Notes: 4

## Slide 5
4. Table of Contents
Chapter | Contents
1 | Installation and Initialize
2 | Web Maintenance Console
3 | Phone Connection
4 | CO Line Connection
5 | IP Configuration : LAN / Wireless LAN / WAN
Notes: 5

## Slide 6
Chapter 1 Installation & Initialize

## Slide 7
11. Appearance
Notes: 7

## Slide 8
Optional card has to be installed during power-off. 1. Power Off. 2. Remove AC cable and open a cover. 3. Install required cards to KX-HTS. Do not turn on power when a cover is opening.
Remove blank panel perfectly. Otherwise optional card cannot be installed. Do not use a knife. Installer may be injured. Use a nipper.
12. Card Installation
This is not OK. (This picture is not KX-HTS.)
More than 1 cm
Notes: 8

## Slide 9
Install KX-HTS on wall. KX-HTS supports router with Wireless LAN function.
13. Wall Mounting
Notes: 9

## Slide 10
KX-HTS PBX has to be initialized at first before programming. Operation and System LED (A) are as follows. 1. Keep pressing Initialize button (B). 2. Power On (D). (a) Amber On : 4 sec (b) Amber rapid flash starts. (c) Green rapid flash starts. 3. During (c), release Initialize button. (d) Green rapid flash : 60 sec 4 flash / sec => After system is initialized, system LED becomes green on.
If only power on, green slow flash starts after (a). It takes for 60 sec. 1 flash / sec
14. Initialize
Notes: 10

## Slide 11
Basic settings are programmed automatically after initialize. - All extension users can make a call to analog CO. - All extension users can receive a call from analog CO.
<Default of Floating Extension Number & Name>
15. Default Data
Notes: 11

## Slide 12
Chapter 2 Web-MC

## Slide 13
21. Connect PC.
Connect PC to LAN port of KX-HTS. IP address of PC is provided automatically by KX-HTS, if PC is DHCP client. DHCP server function of KX-HTS is enabled by default. Access to 192.168.0.101 from PC using web. Web application should be one of following. - Internet Explorer 9-11 - Firefox - Chrome
Smart-phone and Tablet are not recommended.
Notes: 13

## Slide 14
22. Log-in.
Username : INSTALLER Password : 1234 Click [Login]
Notes: 14

## Slide 15
23. Start Easy Set-up.
1. Select language. 2. Select location. This selection is not required and not displayed usually. 3. Change password from “1234”. 4. Click [Start Setup Wizard].
Notes: 15

## Slide 16
24-1. Step 1
1. Select correct time zone and time. 2. Click [Next].
If time zone is incorrect, e-mail may not be sent correctly.
Notes: 16

## Slide 17
24-2. Step 2
1. Select parameter. (Default is OK.) 2. Click [Next].
When “None” is selected for Local Access, “0” or “9” is not required to call trunk. This also can be effective by full programing mode later.
Notes: 17

## Slide 18
24-3. Step 3
1. Select parameter. (Default is OK.) 2. Click [Next].
Notes: 18

## Slide 19
1. Select international access code to restrict calling by TRS. 2. Dialing type is for USA. (Default is OK for other area.) 3. Click [Next].
TRS = Toll Restriction / Call Barring
24-4. Step 4
Dialing plan of PSTN in USA is very complicated.
Notes: 19

## Slide 20
24-5. Step 5
1. Click [Finish]. (Default is OK.)
Notes: 20

## Slide 21
25. Finish Easy Set-up.
1. Click [Skip] to continue programming.
Notes: 21

## Slide 22
Easy Set-up is available only one time after initialize. Full programming mode is available from next connection.
If software of KX-HTS is not latest, it is important to upgrade software to latest version now after Easy Set-up. See step by step guide No.9 for details. It is better to initialize and do Easy Set-up again after version up just in case for new installation.
26. Web-MC Full Programming
Notes: 22

## Slide 23
Chapter 3 Phone Connection

## Slide 24
L2 Switch LAN
103 104 …. 122 101 102 124 123
Total 24 KX-HDV phone and Analog SLT phone can be connected automatically without any programming. - SIP phone registration is required manually for other SIP phone including KX-NTV. - Extension 101 and 102 are for KX-HDV. 103 to 124 are for SLT. - If more than 2 KX-HDV phones are connected, L2 Switch is required and larger extension number is used for KX-HDV automatically instead of SLT. SLT port of the extension does not work.
31. Connect Phones.
KX-HTS
101 102 103 104 …. 124
Analog line LAN cable
KX-HTS
For example, 4 KX-HDV phones and 8 SLT phones can be connected without optional 8-port SLT card. Virtual card installation (like KX-NS) is also not required.
Notes: 24

## Slide 25
If KX-HDV phone has been already registered to other SIP server or SIP carrier, it is required to initialize it in order to connect to KX-HTS.
1. Select “System Settings”. 2. Dial #136. 3. Select “Yes”.
32. Initialize KX-HDV Phone.
Notes: 25

## Slide 26
Fax has to be enabled for analog SLT port by programming. Fax data transmission does not work by default.
33. Connect Fax.
T.38 is not supported for SIP trunk and SIP extension. G.711 and analog line are available for fax. 4 analog trunks (CO) and 8 analog extensions (SLT) are pre-installed by factory.
<Apply> is required for any programming.
Notes: 26

## Slide 27
Flash from analog SLT phone has to be adjusted. On-hook roughly after talking becomes “Flash” sometimes. This becomes cause of unexpected transferring or holding a analog CO. This can be reduced by programming for range of Flash.
34. Adjust Flash Time of SLT.
Hold recall starts immediately after Flash + On-hook. If PBX is other Panasonic KX PBX and SLT flash mode is 1, hold recall starts after 60 seconds as “Ghost call”.
If the extension talked with other extension or SIP trunk, call is disconnected automatically because KX-HTS can detect disconnect from other party. 504ms (Min) and 208ms (Range) if Flash of SLT in your market is 600ms for example.
Notes: 27

## Slide 28
Chapter 4 CO Line Connection

## Slide 29
Unused analog CO port has to be disabled. Select “No Connect”. When unused analog CO is selected automatically by Local Access operation (9/0), user cannot call through PSTN.
41. Disable unused Analog CO.
101 103 Dial 9/0-012- 345- 6789
012- 345- 6789
PSTN
KX-HTS
PSTN = Public Switched Telephone Network
Notes: 29

## Slide 30
Dialing plan for Analog CO and SIP trunk has to be programmed for SLT user. SLT user has to wait for 10 seconds (default) after dialing all digits without this programming.
Local access number (9/0) has to be added. If dialing does not match with any entries, time-out is applied.
42. Assign PSTN Dialing Plan.
101 103 Dial 9/0-012- 345- 6789 and wait for 10 seconds.
012- 345- 6789
PSTN
KX-HTS
Notes: 30

## Slide 31
SIP phone including KX-HDV can call without waiting and without programming, if operation is dialing at first and off-hook like operation of cellular phone.
This programming in the previous page is applied to KX-HDV also for operation : Off-hook and dialing.
Dialing plan for following features are assigned automatically for SLT and KX-HDV. Extension call / Paging call / Call pick up Call Park / Speed Dial
If ARS is used, this programming in previous page is applied to dial before ARS modification.
43. PSTN Dialing Plan - Condition
Notes: 31

## Slide 32
Analog CO connection can be confirmed by calling PSTN using KX-HDV phone or analog SLT phone actually. When CO button of KX-HDV is pressed, dial tone is made by KX-HDV virtually. (No dial tone from PSTN.)
<KX-HDV> Dial 80 + CO number (1-8) + PSTN telephone number and Off hook. => Call starts.
<SLT> Off hook and Dial 80 + CO number (1-8) + PSTN telephone number. => Call starts after 10s.
44. Connect Analog CO and Confirm it.
101 103 Dial 803-012- 345- 6789 and off hook.
012- 345- 6789
PSTN
KX-HTS
Notes: 32

## Slide 33
Chapter 5 IP Configuration

## Slide 34
KX-HTS works as router with PBX.
50. LAN / Wireless LAN / WAN
Internet
WAN L2 Switch LAN
PSTN
KX-HTS
Internet
Notes: 34

## Slide 35
IP address of IP terminal on LAN of KX-HTS is assigned automatically because KX-HTS supports DHCP server by default.
51. LAN
Notes: 35

## Slide 36
SSID and Security Key have to be programmed using Web-MC to connect PC, tablet, smart-phone and so on using Wireless LAN. Default of SSID is “KX-HTS”.
52. Wireless LAN : SSID
Notes: 36

## Slide 37
SSID and Security Key have to be programmed using Web-MC to connect PC, tablet, smart-phone and so on using Wireless LAN. Security key is not common by default to prevent from unexpected access.
53. Wireless LAN : Security Key
Security Key :
Connection is also available using this button of router.
Notes: 37

## Slide 38
If PC has to be connected to Wireless LAN for Easy Set-up after initialize, it can be connected by Setup button without security key. 1. Select “KX-HTS” as SSID by PC. 2. Press this button of KX-HTS. (C) is the button.
54. Wireless LAN : Setup button
Security Key :
Connection is also available using this button of router.
Notes: 38

## Slide 39
WAN port can be connected to internet by PPPoE usually. Ask User Name and Password to your internet provider.
55. WAN for Internet
KX-HTS
Internet
YouTube etc
Notes: 39

## Slide 40
Office
SIP Software phone L2 Switch LAN : 192.168.0.xxx
WAN 192.168.22.99 for example
WAN port of KX-HTS has to be connected to LAN of existing router as DHCP client or using fixed IP address.
56. Connection to LAN of Existing Router
PSTN
KX-HTS
Internet
WAN Existing Router LAN:192.168.22.xxx
Notes: 40

## Slide 41
WAN Existing Router LAN : 192.168.0.xxx
When same IP address is used for LAN of KX-HTS and LAN of existing router, LAN of KX-HTS does not work correctly. Program different segment of IP address to LAN of KX-HTS.
57. LAN of Existing Router - Condition
WAN : 192.168.0.99 L2 Switch LAN : 192.168.0.xxx to 192.168.11.xxx
KX-HTS
Internet
192.168.0.101 to 192.168.11.101
Dealer does not need to discuss with IP network administrator of existing router about IP address of each IP phone because segment is different.
Notes: 41

## Slide 42
58. Change IP address of LAN.
WAN : 192.168.0.99 L2 Switch LAN : 192.168.0.xxx to 192.168.11.xxx
KX-HTS
192.168.0.101 to 192.168.11.101
Notes: 42

## Slide 43
Thank you !

## Slide 44
Revision
Date | No. | Change
June 30, 2015 | All | First draft
July 23, 2015 | All | 2nd draft
July 28, 2016 | Chapter 3 & 4 | Page was sorted. Some pages were moved to step by step guide No.4.
 | Chapter 5 | GUI for programing was added.
 | Chapter 6 | Chapter 6 was moved to 56 and 57 in chapter 5.
 | All | First official release
August 8, 2016 | 33 (Page 26) | <Apply> is required for any programming.
 | 34 (Page 27) | Example was revised.
 | 56 (Page 40) | Example of IP address was revised.
 | 58 (Page 42) | Explanation to change IP address was added.
Sept 1, 2016 | 24 (Page 17) | Explanation was added for “0 or 9”.
Notes: 44